## Slide 1: S32K touch sense Solution keyboards and slider
12th november 2018
Rev 1.0
Automotive Microcontrollers & Processors

## Slide 2: solution

## Slide 3: Solution
Introducing NXP self-capacitance touch sense method supporting:
  Touch pads (buttons)
  Slider
Based on S32K1xx family members, capable of driving up to 30 electrodes
Satisfy requirements of:
  70uA MCU average current consumption
  100ms reaction time
  Sensitivity tuned for 2mm plastic glass overlay on a top of the electrodes
  EMI test with florescent lamp ON

## Slide 4: Demo Features
Multiply sampling & signal averaging
Advanced filtering
Thresholds relative to baseline to compensate an environment humidity and temperature change
Optimized solution for small as well as large keypads:
  6pads keyboard with 5 position 60mm slider consisting of 2 electrodes
  7pads keyboard
  S32K144EVB Q100 2pad small keypad enabled

## Slide 5: FreeMASTER – Visualization and Parameters Tuning Tool
Variable Watch
Variable Display
Touch button electrodes

## Slide 6: FreeMASTER – Visualization and Parameters Tuning Tool
Variable Watch
Variable Display
Slider electrodes

## Slide 7: FreeMASTER – Visualization and Parameters Tuning Tool
Variable Watch
Variable Display
Slider data

## Slide 8: Electrode Data Processing
Thresholds
Electrode Signal
DC Tracker
LP Filter
Electrode
Touched
Touch Report

## Slide 9: How to Get demo Running?

## Slide 10: Demo Set-Up
Connect demo board with PC using USB cable
Open project related FreeMASTER page
Establish communication

## Slide 11: Demo Operation
Touch keyboard pads or slider
Monitor on-board RGB LED color
  Touch pad touch event – single LED color
  Slider touch event – LED color is changing along with finger position
  Touch pads have bigger priority than slider
Check blue background lighting

## Slide 12: Demo Operation - Position Determination On 5 Segment Slider
Electrode 0
Electrode 1
Slider difference data threshold 0
Slider difference data threshold 1
Slider difference data threshold 2
Slider difference data threshold 3
Slider difference data
Software perspective:
Slider difference data change when moving finger across the slider
Seg. 1
Seg. 2
Seg. 3
Seg.4
Seg.5
Software layer
Hardware layer
User perspective:
Moving finger across the slider from el. 0 to el.1

## Slide 13: Demo software

## Slide 14: Software
Electrode raw data available for custom operation
Configurable to operate customer hardware design
FreeMASTER – application parameters tuning tool